## Slide 1
SLIDE 1 · PROBLEM & MOTIVATION
When a Wind Turbine Goes Dark, How Much Energy Was Lost?
Turning missing blackout data into an auditable Business Interruption insurance claim.
Goal: Accurate, transparent loss claims that any insurance adjuster can verify | 72h Fleet Outage Loss: 283.9 MWh
1. The Grid Outage
• Cable damage or grid faults disconnect the wind farm from the grid.
• Turbines stop generating electricity and revenue drops to zero.
2. The Sensor Blind Spot
• Normally, we calculate lost energy using the turbine's own wind sensor.
• During a complete blackout, that wind sensor is offline too (missing NaN data).
3. Our Automated Solution
• Learn how neighbouring wind parks (Park O & Park H) relate to our turbine before the outage.
• Reconstruct the missing wind speeds and calculate lost MWh through the power curve.

## Slide 2
SLIDE 2 · EXPLAINABLE ARCHITECTURE
Why Our Model Is Simple, Physical & 100% Explainable
Prioritizing explainability — one clean equation per turbine instead of a black box.
Formula Structure: v_Target = w0 + w_O · Speed(Park O) + w_H · Speed(Park H) + Direction (u, v) | 100% Transparent
One Readable Equation
• Uses Bayesian Ridge Regression.
• Every turbine gets a single linear formula you can verify on a calculator.
• Zero hidden layers or opaque decision rules.
Why Aggregate into Parks?
• Turbines in the same park (O1–O2 or H1–H5) feel >96% identical wind.
• Separate turbine weights fight each other and create fake negative numbers.
• Park medians give clean ~40% / ~40% weights and survive single-sensor dropouts.
Better Than Other Models
• vs. LightGBM (450 Trees): Black box that fails seasonal shifts (-20% error) and cannot be audited.
• vs. Raw OLS Regression: Suffers from unphysical negative weights.
• Explainability is key for insurance sign-off.

## Slide 3
SLIDE 3 · NATIVE UNCERTAINTY QUANTIFICATION
Native Bayesian Uncertainty: Two Bands, Zero Crossing
Uncertainty comes directly from Bayesian probability math — not ad-hoc quantile trees.
T1 Outage Example: Central P50 = 75.3 MWh · 95% Formula CI = 73.3–77.4 MWh · 80% Gust Band = 26.8–154.8 MWh | Calibrated at 82.7%
Why Native Bayesian Beats Quantile Models
• Quantile Models (LightGBM): Train 3 separate black boxes (P10, P50, P90). Because they don't share math, curves can cross (P10 > P50).
• Native Bayesian Ridge: Outputs a complete Gaussian bell curve (mean μ & spread σ) at every 10-minute step.
• Guaranteed Consistency: Any percentile (50%–99% slider in our app) is smooth and mathematically cannot cross.
Two Uncertainties Separated Automatically
• 1. 95% Coefficient CI (Dark Inner Band — ±2.0 MWh): 'How sure are we about our formula?' Pinpointed tightly by 12,400+ training intervals.
• 2. 80% Predictive Band P10–P90 (Light Outer Band): 'How gusty is a single 10-minute step?'
• Over a 3-day outage, random 10-minute wind gusts cancel out — so true energy stays close to P50.

## Slide 4
SLIDE 4 · CROSS-VALIDATED ACCURACY
Robust Accuracy via 5-Fold Cross-Validation
Tested across all 86 operational days (12,421 intervals) without permanently withholding training data.
Why Background 5-Fold CV? Tests every time block out-of-sample while the final model trains on 100% of history | Zero Data Wasted
Turbine T1 (5-Fold CV)
• Wind Speed MAE: 0.990 m/s
• Wind Speed RMSE: 1.338 m/s
• Power MAE: 492.6 kW
• 80% Band Coverage: 82.4%
• 5-Fold Energy Error: -12.78%
• 72h Outage Loss: 75.32 MWh
Turbine T2 (5-Fold CV)
• Wind Speed MAE: 0.880 m/s (Best)
• Wind Speed RMSE: 1.182 m/s (Best)
• Power MAE: 453.4 kW
• 80% Band Coverage: 82.8%
• 5-Fold Energy Error: -8.77%
• 72h Outage Loss: 117.16 MWh
Turbine T3 (5-Fold CV)
• Wind Speed MAE: 0.893 m/s
• Wind Speed RMSE: 1.194 m/s
• Power MAE: 440.2 kW (Best)
• 80% Band Coverage: 83.0%
• 5-Fold Energy Error: -11.35%
• 72h Outage Loss: 91.46 MWh

## Slide 5
SLIDE 5 · PHYSICS & BONUS FEATURES
Physics Addons & All 3 Bonus Challenges
Going beyond wind speed with atmospheric physics, smart filtering, and instant claim emails.
Live Demo: Interactive Streamlit App with plain-English '?' guides, manual calendars & 10-min certainty explorer | BayWa r.e. Ready
1. Direction & Air Density Physics
• Wind Vectors (u, v): Fixes the 359° ↔ 1° compass jump and captures hill & wake sheltering.
• IEC 61400-12-1 Air Density: Uses live Temperature & Pressure from Park H (97.9% regional match) to adjust blade push for thin warm vs. dense cold air.
2. Auto Reference Selection
• Automatically scans all uploaded reference files (O1–O2, H1–H5).
• Detects and removes any reference turbine that is offline during the outage.
• Ranks references by correlation and shared training days.
3. One-Click Insurance Claim
• Generates a clean claim notice with only relevant data: outage times, reference turbines, Estimated MWh, and 5-Fold CV proof.
• Includes an 'Open in Default Mail App' button that launches your email client pre-filled.